## Slide 1: Sparsity Techniques

## Slide 3
Fault Study
Load Flow Study
Stability Study
3 Studies in Power System Analysis
Load Flow is a Static Study (Static Study means not change at each and every instant, it is constant)
Stability Study is a Dynamic Study, because any state our power may be unstable.

## Slide 5: Load Flow Study Is a Static or Dynamic Study
Load Flow is a Static Study (Static Study means not at each and every instant, it is constant)
Stability Study is a Dynamic Study, because any state our power be a unstable.

## Slide 7: Sparsity of Y-Bus Matrix
Sparsity of the Ybus matrix is defined as the ratio of total number of zero element to the total number of element in the Ybus matrix.
Calculation of Sparsity of Y-Bus
Property1:
If number of bus is 3, size of the matrix will be 3 3
If number of bus is n, size of the matrix will be n n.
Total number of element in the matrix = n n = n2
Total number of diagonal element = No. of bus = n
All the diagonal values in the matrix are non-zero.

## Slide 9
Calculation of Sparsity of Y-Bus
Property2:
Ybus matrix are symmetric
Y12 = Y21 and Y13 = Y31
If a Transmission line available in between bus 1 & 2 than
Y12 & Y21 are non-zero element
Number of non-zero element = 2 No. of Transmission line
Total number of non-zero element in the Ybus matrix = No. of diagonal element + ( 2 No. of Transmission line)
Number of branches (transmission line) = (Number of buses – number of non-zero element)/2

## Slide 11
Sparse (Zero Values) Matrix In Power System

## Slide 13
QUIZ: Suppose we used 3-admittance buses and than how many transmission lines.
Ans: Transmission Lines are also 3.
QUIZ: If we reduce the number of Transmission line from 3 to 2 than which elements are possible to be zero?
Ans: Any two elements should be zero but both elements are same such as (Y12 and Y21 or Y13 and Y31 than remaining non-zero is)

## Slide 15: Q: The Y bus matrix of a 100 bus interconnected system is 90% sparse. Then find the number of non zero in the Y bus matrix?
SOLUTION

## Slide 17: Q: Check Sparsity with Previous Solved Example of Bus Admittance Matrix
FIGURE 1: The impedance diagram of a simple system

## Slide 19: Q: a 1000 x 1000 bus admittance matrix for an Electric Power System has 8000 non-zero elements. The minimum number of branches (transmission & transformer) in this system are
Number of branches (transmission line) = (Number of buses – number of non-zero element)/2
SOLUTION
Number of branches (transmission line) = (1000 – 8000)/2 = 3500 --- Answer